CRPC #690

CAPITOL REGION PURCHASING COUNCIL

INVITATION FOR BID

ASPHALT PAVEMENT CRACK SEALING

BID SPECIFICATION

I.  MODIFICATIONS TO GENERAL TERMS AND CONDITIONS

INTENT

The Capitol Region Purchasing Council, on behalf of certain CRPC members, requests bids for ASPHALT PAVEMENT CRACK SEALING using the hot pour method, for the contract period of October 1, 2019 through September 30, 2020.  Each respective CRPC member will make its own awards and payments according to the terms and conditions set forth in these specifications.  A written order from each CRPC member will be required before any work is started, and shall contain information concerning the quantity and type of asphalt pavement crack sealing required, the desired materials to be used, the preferred work schedule, and any other relevant data. This bid is intended for projects that do not meet the threshold for State of Connecticut prevailing wages as codified in the General Statute section 31-53 and 31-53a.  Projects that meet or exceed the threshold shall not be purchased through this bid.

Vendors who wish to submit a bid for the Cold Applied Mulch Sealing method may submit an alternate bid which contains documentation on Organic Cover Material, Mulch Seal Liquid Material, and equipment.

In general, specifications for asphalt pavement crack sealing found in ASTM D6690 will apply.

BID AWARD

A bid award shall be made by each respective CRPC member to the lowest responsible, responsive bidder(s) for their specific needs.  The lowest responsible bidder is that person or firm whose bid to perform the work is lowest, who is qualified and competent to do the work, whose past performance of work is satisfactory to the CRPC member and whose bid documents comply with the procedural requirements stated herein.  The award process may also include additional considerations such as the information provided on the bid forms and the bidder’s perceived ability to fulfill his/her obligations as prescribed by these specifications.  The issuance of a Purchase Order from a CRPC member constitutes an award, and such awards may be made to one or more vendors.

Each bidder must be prepared to show evidence of having satisfactorily carried out a similar contract, as inability to do so may be cause for rejection.  Note that service and scheduling shall be major factors in awarding the contract, and shall consist of the contractor’s availability to return to do small jobs during the contract period, as well as to perform work during off-hours (e.g., nights, weekends). Note that the CRPC members reserve the right to make their awards on a section-by-section basis in order to take advantage of the most favorable bid price for each item.

ESTIMATED QUANTITIES

The quantities specified herein are estimates only and have been provided for the purpose of competitive bidding.  Actual quantities will be contingent upon the total number of CRPC members which decide to make an award off this bid (as participation is voluntary), the needs of the using departments of the various CRPC members and changes in State and Local Regulatory Agency’s regulations.  Furthermore, budget reductions may make it impossible for a CRPC member to undertake some or all of the proposed work.  The determination of the type of asphalt pavement crack sealing to be used will be made by the individual CRPC member under the guidance of the State and Local Regulatory Agencies.

INSURANCE

All respondents are required to submit, with their bids, the endorsement page of your insurance policy(ies) (or an equivalent piece of documentation) which demonstrates the firm’s current coverages and limits for General Liability, Automobile Liability and Worker’s Compensation Insurance, as well as the Certificate of Insurance.

BID SURETY

A bid bond is not required for this bid.  A performance bond in the amount of one hundred percent (100%) of each Purchase Order may be required of the successful bidder, if the awarding town requests one.

II.  TECHNICAL SPECIFICATION, ADDITIONAL REQUIREMENTS

1.	GENERAL DESCRIPTION OF WORK TO BE ACCOMPLISHED

The awarded contractor(s) shall be responsible for providing all labor, equipment, and materials necessary to clean and seal cracks in existing asphalt pavements and milled roads, using the hot pour materials method. All work performed by the contractor will be approved by the CRPC member’s appointed Supervisor .

2.	SCOPE OF SERVICES

All-inclusive bids shall be submitted, covering labor, equipment and materials for the items listed in the bid response.  Such work shall include, but is not limited to, related cleaning, road preparation, traffic control and clean-up.

- Equipment

The equipment required is: Air Compressor, melting kettle, application wand and show, hot air lance, and shall conform to the requirements provided by the awarding entity. On the information sheet, each respondent shall note all equipment that he/she owns and will use in performing this contract.  The respondent shall also indicate any other machines available to him/her through lease, etc.

Maintenance

The Contractor shall keep and maintain their work in good repair for a period of ninety (90) days from the date of completion of the work on the respective streets. It is agreed and understood that the Contractor will at any time during this period, upon notification in writing from the Supervisor, and without expense to the CRPC member, immediately execute all repairs which may be necessary, as determined by said Supervisor by reason of defective workmanship or pavement/roadway use.

- Cleaning/Road Preparation

The awarded Contractor shall clean the existing asphalt road surface of all dirt, sand, oil, grease and loose materials by brooming, blowing, or flushing with pressurized water as approved in advance by the awarding entity.  All unsealed cracks, all previously sealed cracks with the surface of the existing sealant greater than or equal to ¼” below the surface of the surrounding pavement, and all previously sealed cracks exhibiting cracks, holes, voids and separation from the adjacent pavement shall be sealed. Immediately prior to sealing, all cracks shall be thoroughly cleaned of all foreign material. When cracks show evidence of vegetation, the vegetation shall be removed and sterilized by the use of a propane torch unit, eliminating all vegetation, dirt, moisture and seeds.  No crack-sealing material shall be applied in wet cracks, or, where frost, snow or ice is present. The pavement temperature shall be above 40 degrees Fahrenheit (4 degrees Celsius) at the time of the installation of the poured sealing material.

### Traffic Control:

All traffic control methods and devices are to be in compliance with the current edition of the Manual of Uniform Traffic Control Devices. All adjustments to traffic operations are to be coordinated with the Director of Public Works for the awarding entity. The Contractor shall maintain and protect traffic in the project area in accordance with the requirements and regulations of the applicable Federal, State and Local Regulatory Agencies and these specifications. It shall be the sole responsibility of the Contractor to notify the State and Local Regulatory Agencies of the awarding entity at least 72 hours in advance of changes in traffic patterns due to the reduction of pavement widths or other traffic obstructions. The Contractor shall furnish, install, maintain, adjust, and remove all signs, suitable barricades, flashers, and traffic cones, as necessary to carry out the traffic routing plan and maintain vehicular and pedestrian traffic. All of this work shall meet with the approval of all the State and Local Regulatory Agencies.

The road may be restricted during the construction period but must be opened at the end of each day. The road must be made passable as soon as possible.

In addition, access to emergency vehicles, police, rubbish removal trucks, school buses and mail delivery vehicles must be maintained.

When requested to do so by the CRPC Member, the Contractor shall furnish the CRPC member with a plan or a written statement of methods, which the Contractor proposes to use, and said plans or methods shall be approved by the Supervisor before any work proceeds.

The cost associated with this item shall not be paid separately, but shall be included in the bid items.

3.	EXPERIENCE

Each respondent must submit satisfactory evidence as part of their bid proposal demonstrating experience repairing/sealing asphalt pavement cracks on public roads and knowledge of regulations established by the State and Local Regulatory Agencies, including the most recent regulations.  The Contractor shall further guarantee that any employee operating asphalt pavement crack sealing equipment is experienced in operating a machine of this type and competent in its use.

A list of at least three (3) municipalities/public agencies where this type of work has been performed during the past two (2) years shall be furnished, including contact persons and phone numbers. (See the bid specific Information Sheet.)

4.	TIME OF STARTING AND COMPLETION

The Contractor may be requested to start work within seven (7) calendar days of receipt of order, depending on the agreement with the Supervisor of any single CRPC member awarding such contract.  All work under any contract awarded as a result of this bid shall be completed within thirty (30) calendar days of receipt of the order unless a specific agreement with a particular Supervisor provides for a later completion date.  If physical conditions prevent adherence to this time schedule, the Supervisor of the particular CRPC member shall make arrangements necessary for performance of the work.  It is understood that a CRPC member may take appropriate action if an unreasonable delay is encountered beyond the thirty (30) calendar day period mentioned above.

It is also understood that should delays occur, the Contractor will prioritize rescheduling efforts to expedite completion and minimize CRPC member exposure from unmarked roadways.

Note: Equipment breakdown shall not be considered a valid cause for a time extension request.  The contractor shall be expected to have backup equipment available.

5.	PAVEMENTS TO BE SEALED

Sealants shall be applied mainly on sheet asphalt and milled road pavements.

6.	MATERIALS

All materials shall be in accordance with the State of Connecticut, Department of Transportation, Standard Specifications for Roads, Bridges and Incidental Construction Form 816, as amended unless otherwise noted:

Joint Sealer

The hot poured rubberized sealant material shall meet requirements of ASTM D6690, or the latest edition. CRPC members may require joint material samples to be submitted prior to the start of work.

Respondents are asked to include, as part of their response, a manufacturer spec sheet for the sealant that will be used to perform the work.

Crack Sealant

Glenzoil 20 Plus by Emulso Corp. or equivalent crack sealant barrier material.

Respondents are asked to include, as part of their response, a manufacturer spec sheet for the                    sealant that will be used to perform the work.

Post-Sealing Spray

Members may require a post-seal anti-stick spray agent, to prevent sealing materials from sticking to tires.

7.	EQUIPMENT

Equipment used in the performance of the work required shall be subject to the approval of the awarding entity, and maintained in satisfactory working condition at all times.

Air Compressor:

Air compressors shall be capable of furnishing not less than 185 cubic feet of air per minute and shall be equipped with traps that will maintain the compressed air free of oil and water.

Melting Kettle:

The joint sealant material shall be heated in a melter constructed as a double boiler, with a space between the inner and outer shells filled with oil or other heat transfer medium having a flash point of not less than 600 degrees. The equipment shall include positive temperature controls, automatic and continuous mechanical agitation, recirculation pumps, and thermometers for continuous reading of temperature of both the sealing compounds and the heat transfer medium. The melter shall be equipped with a thermostat to maintain the sealant compound within the range of temperatures specified by the manufacturer. Respondents are asked to include, as part of their response, a manufacturer spec sheet for the material that will be used to perform the work.

##### Application Wand and Shoe and Hand Pouring Pots

Application shoes that are worn shall be replaced. The application shoe shall produce a band aid type of appearance of at least 1” wide on either side of the crack, as well as filling the crack. The height of the sealant above the crack must not exceed 1/8”. Hand pouring pots must be equipped with mobile carriage and rubber shoe, and have a flow control valve which allows all cracks to be filled to refusal, so as to eliminate all voids or entrapped air, and not leave unnecessary surplus crack sealer on pavement surfaces.  Respondents are asked to include, as part of their response, a manufacturer spec sheet for the material that will be used to perform the work.

Hot Air Lance

Hot air lance shall be a propane torch unit which operates at 3,000 degrees Fahrenheit and a gas velocity of 3,000 feet per second.

8.	VENDOR PERFORMANCE/LIABILITY FOR SERVICE FAILURES

Failure of any successful bidder to adhere to the specifications, prices, terms or conditions of their agreement during the course of the contract period may preclude such bidder from bidding on future CRPC bids in addition to any action that municipalities may take as a result of the vendor’s failure to perform.  It should be noted that the awarded vendor shall assume full responsibility for the negligence of any sub-contractor(s) utilized to fulfill any and all obligations under resulting contracts.  Moreover, if the contractor fails to provide the contracted services within the time specified or if the services are rejected by the municipality, the municipality may obtain such services or any part thereof from other sources in the open market or on contract.  Should the new price be greater than the contract price, the difference will be charged against the contractor.  Should the new price be less, the contractor shall have no claim to the difference.